## Slide 1
Project 21: Counterflow C₂H₄/Air Diffusion Flame
Effect of H₂O dilution and residence time on PAH formation
Mechanism: CRECK C₂H₄ HT + Soot (368 sp, 14228 rxn)
Pressures: 1, 10 bar | H₂O: 0, 4, 8, 12% | 4 residence times
IIT Roorkee

## Slide 2: Configuration
• Geometry: counterflow non-premixed, plate separation L = 2 cm
• Fuel stream: C2H4 + H2O (varying X_H2O = 0, 4, 8, 12% mole)
• Oxidizer stream: air (X_O2 = 0.21, X_N2 = 0.79)
• Inlet temperatures: T_fuel = T_oxidizer = 300 K (assumed)
• Pressures: 1 bar and 10 bar
• Residence time varied via fuel mdot ∈ {0.06, 0.10, 0.14, 0.20} kg/m²·s
(oxidizer mdot held fixed at 0.30 kg/m²·s)
• Total cases: 2 × 4 × 4 = 32
• Kinetic model: CRECK C2H4 HT+SOOT, 368 species, 14228 reactions
(PAH chain: benzene → naphthalene → phenanthrene → pyrene)

## Slide 3: Methodology
1. Convert CRECK CHEMKIN files to Cantera YAML (ck2yaml).
2. Strip discrete-sectional soot bins (BIN species) lacking thermo data;
keep full gas-phase + PAH chemistry up to C16H10 (pyrene).
3. Solve a 'seed' counterflow flame at p=1 bar, x_H2O=0 (~ baseline mdot).
4. Sweep continuation: pressure → H2O fraction → fuel mdot.
Each new case restores the previously converged solution.
5. Extract peak T, residence time τ, peak PAH mole fractions, locations.
6. Tabulate to CSV, plot, assemble report.

## Slide 4: Peak T vs H2O dilution @ 1.0 bar
Peak flame T decreases with H2O dilution due to thermal sink and reduced fuel concentration.

## Slide 5: Peak Benzene (A1) vs H2O @ 1.0 bar
Effect of H2O on Benzene (A1) formation. Increased OH from H2O dissociation suppresses PAH precursors.

## Slide 6: Peak Naphthalene (A2) vs H2O @ 1.0 bar
Effect of H2O on Naphthalene (A2) formation. Increased OH from H2O dissociation suppresses PAH precursors.

## Slide 7: Peak Phenanthrene (A3) vs H2O @ 1.0 bar
Effect of H2O on Phenanthrene (A3) formation. Increased OH from H2O dissociation suppresses PAH precursors.

## Slide 8: Peak Pyrene (A4) vs H2O @ 1.0 bar
Effect of H2O on Pyrene (A4) formation. Increased OH from H2O dissociation suppresses PAH precursors.

## Slide 9: Pyrene peak heatmap @ 1.0 bar
Pyrene formation peaks at low H2O and low mass flux (long residence time).

## Slide 10: Peak T vs H2O dilution @ 10.0 bar
Peak flame T decreases with H2O dilution due to thermal sink and reduced fuel concentration.

## Slide 11: Peak Benzene (A1) vs H2O @ 10.0 bar
Effect of H2O on Benzene (A1) formation. Increased OH from H2O dissociation suppresses PAH precursors.

## Slide 12: Peak Naphthalene (A2) vs H2O @ 10.0 bar
Effect of H2O on Naphthalene (A2) formation. Increased OH from H2O dissociation suppresses PAH precursors.

## Slide 13: Peak Phenanthrene (A3) vs H2O @ 10.0 bar
Effect of H2O on Phenanthrene (A3) formation. Increased OH from H2O dissociation suppresses PAH precursors.

## Slide 14: Peak Pyrene (A4) vs H2O @ 10.0 bar
Effect of H2O on Pyrene (A4) formation. Increased OH from H2O dissociation suppresses PAH precursors.

## Slide 15: Pyrene peak heatmap @ 10.0 bar
Pyrene formation peaks at low H2O and low mass flux (long residence time).

## Slide 16: Pressure effect on pyrene
Higher pressure dramatically increases PAH formation due to higher reactant density and longer chemistry timescales.

## Slide 17: Pressure effect on peak T
Pressure has only a modest effect on adiabatic flame T compared to its strong effect on PAH chemistry.

## Slide 18: Axial profile @ 1.0 bar, no H2O, longest τ
Temperature, benzene, naphthalene, phenanthrene, pyrene profiles across the flame.

## Slide 19: Discussion: Effect of H₂O on PAH formation
• H2O dilution reduces peak flame temperature → slows pyrolysis kinetics
(rate-limiting step for benzene formation via C3H3 self-recombination
and HACA pathways)
• H2O thermally dissociates near the flame front, providing additional OH.
OH attacks PAH precursors (C2H2, C3H3, C4H2) and reduces benzene yield.
• Net effect: monotonic decrease of peak C6H6, C10H8, C14H10, C16H10
with H2O fraction at both 1 and 10 bar.
• Suppression is stronger for heavier PAHs (pyrene) than benzene because
HACA growth depends multiplicatively on smaller-PAH concentrations.
• Pressure effect: 10 bar greatly amplifies all PAHs (higher reactant
density, longer chemistry times). Adding H2O is more effective at
suppressing PAHs at 10 bar than at 1 bar.
• Residence-time effect: longer τ → more PAH (benzene → naphthalene →
pyrene chain has time to propagate). Effect amplified at higher P.

## Slide 20: Thank you